## Slide 1
Reading the Radar
A hands-on guide to what weather radar sees — and misses
Clouds4Africa · July 2026
Sebastián Torres — CIWRO / University of Oklahoma
Notes: Welcome. This deck is the short briefing to run before each hands-on block. Each block is slider-driven notebooks — no coding — followed by a real radar case, all at three depth levels.

## Slide 2
The five blocks: one measurement, end to end
1 · The beam in space where the echo comes from — spread, height, bending, blockage
2 · One measurement how big a value is, and whether it can be detected
3 · Range, velocity & ambiguity how far and how fast — and where the sampling breaks
4 · Wavelength, weather & the scan what the wavelength decides; building a volume scan
5 · Two polarizations what the echo is made of — rain, hail, melting layer
Each block: 3–4 slider widgets + a real-data case · three depth levels (Basic · A little further · Going deeper).
Notes: The blocks follow the life of one measurement, end to end. Blocks 1–4 are the live workshop; Block 5 (dual-pol) is the take-home bonus, flagged in amber.

## Slide 3
01
BLOCK 01
The beam in space
Where does the echo actually come from?
A radar doesn't measure a point — it measures a beam that spreads, climbs, bends, and can be blocked.
Notes: Set the frame: every later block assumes you know the beam is a physical volume in space. Keep this one intuitive.

## Slide 4
What a radar measures
Pulse and echo
Transmit a short pulse, then listen. Distance comes from the time delay — a later echo is farther away.
The products
Reflectivity (dBZ) — how much and how large the scatterers are — is the focus here. Velocity and dual-pol arrive in later blocks.
Tilt, azimuth, range
The beam points at an elevation (tilt) and azimuth and sweeps a circle to build a PPI; range is distance outward along it.
Notes: Just orientation — most of the audience forecasts but may not have built the mental model of how a value gets made. Thirty seconds each.

## Slide 5
The one idea: the beam is a volume, not a ray
Spreads
θ ≈ 1.27 λ/D — fixed in degrees, so the physical width grows with range.
Climbs
The Earth curves away faster than the beam bends, so it rises with range.
Bends
Refractivity gradients bend the beam; strong ducting traps it and paints false echoes.
Gets blocked
Terrain near the radar clips the beam and shadows everything downrange of it.
Notes: This 2x2 is the spine of Block 1 — the four widgets map one-to-one onto these four behaviours.

## Slide 6
Why it matters
Overshooting
Beyond ~150 km the lowest beam is kilometres up — shallow rain and snow slip underneath unseen.
False echoes
Night-time ducting bends the beam into the ground: clutter appears where there is no weather.
Terrain wedges
Blocked azimuths read low or empty — not because the rain is absent.
“No echo” is not the same as “no weather.”
Notes: Land the operational stakes. The amber line is the sentence you want them repeating back all week.

## Slide 7
What you'll do
Four widgets
Beamwidth · beam height & refraction · anomalous propagation · terrain blockage.
Real data
Four reflectivity tilts of one storm — radial blockage spokes that fill in as the tilt rises; separate real weather from terrain.
TAKEAWAY
A measurement is a beam of finite width that climbs, bends, and can be clipped — so “no echo” ≠ “no weather.”
Notes: Hand off to the notebook. Remind them to run the install and setup cells once, then work the widgets in order.

## Slide 8
Discussion
A colleague points to a blank patch on a radar image and says "no rain there." What would we want to check before agreeing?
We watched blocked spokes fill back in as the tilt rose. If we could keep just one elevation tilt of a storm, should we take the lowest or a higher one — what do we gain and lose, and when might our answer flip?
Notes: Hand off to the notebook. Remind them to run the install and setup cells once, then work the widgets in order.

## Slide 9
02
BLOCK 02
One measurement
How big is a single radar value — and can the radar even detect it?
One pixel on the screen is a chunk of air, not a point.
Notes: Bridge from Block 1: now that we know where the beam goes, ask how big the sample is and whether a faint echo even registers.

## Slide 10
A pixel is a volume average
Depth
Set by the pulse: cτ/2. Fixed with range.
Width & height
Set by the beam: r·θ. Both grow with range.
One value = one volume
depth = cτ / 2
width = height = r·θ
volume ∝ r² (grows fast!)
Notes: The headline: a distant pixel averages a huge box of atmosphere. Volume grows as r-squared — both cross-beam dimensions widen.

## Slide 11
The pulse trade
Short pulse
Fine range resolution (Δr = cτ/2 small)
Less sensitive — less energy
Smaller blind range near the radar
Long pulse
More sensitive — more energy per pulse
Coarse range resolution
Deeper sample, larger blind range
Lengthen the pulse and every gain costs something.
Notes: One slider, three consequences. This is where they internalise that radar design is all trade-offs.

## Slide 12
Detection is not guaranteed
Sensitivity falls with range
Received power ∝ 1/r², so the faintest detectable reflectivity climbs with distance.
Hardware moves the curve
Transmit power, dish size, and wavelength all shift the whole sensitivity curve.
+6 dB
per range doubling — the beam-filled sensitivity law
Notes: Tie it back: a weak distant echo that's missing may be below the noise floor, not absent. Another flavour of 'no echo is not no weather.'

## Slide 13
What you'll do
Three widgets
Pulse width · the resolution volume · the radar equation (sensitivity).
Real data
The 20 May 2013 Moore storm seen by two radars at once — 20 km vs 200 km.
TAKEAWAY
One value is a volume-sized average — a distant pixel is a big spatial average, an underestimated peak, and a detection threshold at once.
Notes: The two-radar case is the controlled experiment: same storm, two ranges, so resolution loss separates cleanly from beam height.

## Slide 14
Discussion
We saw the same storm from 20 km and 200 km look very different. If two radar images disagreed about how intense a storm is, what should we ask about how each measurement was made before deciding which to believe?
A radar shows an echo fading to nothing at its far edge. How many different things could that fading edge mean and how could you tell them apart?
Notes: Hand off to the notebook. Remind them to run the install and setup cells once, then work the widgets in order.

## Slide 15
03
BLOCK 03
Range, velocity & ambiguity
How does the radar know how far and how fast — and where does that break?
Range and velocity come from the same pulse train — and the rate that helps one hurts the other.
Notes: This block is the time-domain twin of Block 1. The key tension: one knob (the PRF) sets two limits that fight each other.

## Slide 16
One pulse train, two jobs
Maximum range
A pulse must return before the next goes out: r_max = c / (2·PRF).
Maximum velocity
The same pulse rate sets the fastest unambiguous speed: v_max = λ·PRF / 4.
Raise the PRF for velocity and you lose range — and vice versa.
Notes: Make sure they see both r_max and v_max depend on the SAME PRF, in opposite directions. That sets up the dilemma.

## Slide 17
The Doppler dilemma
r_max · v_max = c·λ / 8
fixed by wavelength alone — a hard wall
You only ever slide along one curve: long range or high Nyquist velocity, never both at once. A shorter wavelength (C-band) lowers the wall further.
Notes: The single most important equation of the block. Note the wavelength dependence — it returns in Block 4 and matters for C-band Africa.

## Slide 18
Past the ceiling, it folds
Range folding
A storm beyond r_max is misplaced to a shorter range — or, in modern data, simply flagged and dropped.
Velocity aliasing
A storm faster than v_max reads as the wrong speed — even the wrong direction.
These are sampling artifacts to read, not radar faults.
Notes: Pre-empt the misconception: aliasing and folding are not errors. They are predictable consequences of sampling that a reader learns to undo.

## Slide 19
What you'll do
Three widgets
Range folding · the Doppler dilemma · velocity aliasing.
Real data
Hurricane Isabel (2003) — reflectivity and velocity side by side; spot the fold and the smaller velocity disk.
TAKEAWAY
Range and velocity share one pulse train, and r_max·v_max = cλ/8 is a wall — folding and aliasing are artifacts you learn to read.
Notes: In the hurricane case the velocity disk is visibly smaller than reflectivity — that edge is r_max made visible. Pre-SZ-2 data, so folded gates are dropped, not painted.

## Slide 20
Discussion
In the Isabel data we looked for an aliased patch, a spot where the wind seemed to flip suddenly. Once we know to spot it as an artifact, not a real reversal, how does that change the way we'd read a velocity image — and why is a limit we can't remove still worth knowing?
If we had to choose between a radar that sees very far but can't measure fast winds, and one that measures fast winds but only nearby, what kinds of weather would push us toward each?
Notes: Hand off to the notebook. Remind them to run the install and setup cells once, then work the widgets in order.

## Slide 21
04
BLOCK 04
Wavelength, weather & the scan
How does wavelength shape what you see, and how do you assemble a volume?
Your networks run C-band — and here, every choice buys something and pays for it.
Notes: Strongest local hook of the course: most African networks are C-band. This block is the payoff and the synthesis.

## Slide 22
Shorter wavelength, bigger price
S-band · 10 cm
Attenuation negligible
Reaches through heavy cores
Big dish, long range (NEXRAD)
C-band · 5 cm
Attenuation is real
Most African networks
Smaller dish, more sensitive
X-band · 3 cm
Attenuation severe
Cores can be wiped out
Compact / gap-filler radars
A shorter wavelength buys a finer beam from a smaller dish — but rain absorbs and scatters it more.
Notes: Anchor the band the audience actually operates (C). Frame attenuation as the price paid for the smaller-dish advantage.

## Slide 23
The competition
More sensitive
A shorter wavelength detects weaker echoes at the same dish (the 1/λ⁴ term).
But attenuates more
And the loss grows with range — it's a path integral through the rain.
Which band sees a distant storm? Whichever wins the crossover.
Notes: This is the new widget 2. Sensitivity favours short wavelengths; attenuation favours long ones; the crossover decides per situation.

## Slide 24
A scan is many beams in finite time
Cone of silence
Nothing is sampled above the top tilt — a blind cone directly over the radar.
Low-level gap
Below the bottom tilt, distant low-level weather is missed.
Update time
Every added tilt slows the volume — the exact problem phased arrays solve.
Notes: Scan strategy ties the whole course together: vertical detail vs clean velocity (Block 3) vs update speed. No free lunch.

## Slide 25
What you'll do
Three widgets
Attenuation · sensitivity-vs-attenuation · scan strategies.
Real data
Two S/C pairs — where C-band loses to attenuation, and where it wins on sensitivity.
TAKEAWAY
Every gain has a coupled cost: a shorter λ buys sensitivity but pays in attenuation; more tilts trade detail against clean velocity and update speed.
Note: operational C-band radars recover much of the attenuated signal with dual-pol (KDP) — the practical fix, coming in Block 5.
Notes: Close the arc. Mention KDP as the operational answer to attenuation so C-band doesn't look doomed — it's the bridge to dual-pol, which this course doesn't cover.

## Slide 26
Discussion
Across the blocks, one theme kept returning: every radar choice — wavelength, dish, pulse, tilts — buys something and costs something. Which trade-off surprised you most, and could you "fix" it with a better radar, or is the cost baked into the physics?
If someone handed you a single radar image with no other information, what would you now want to know about the radar itself before trusting what the image shows?
Notes: Hand off to the notebook. Remind them to run the install and setup cells once, then work the widgets in order.

## Slide 27
05
BLOCK 05
Two polarizations
What is the echo made of — not just how much?
A single polarization tells you how much is there. Two — horizontal and vertical — tell you what it is.
Notes: New measurement dimension: polarization. Frame it as the modern capability the first four blocks didn't use, and the one most relevant to a rainfall-focused C-band audience.

## Slide 28
Two polarizations, one volume
Horizontal and vertical
The radar sends and receives at both polarizations. On its own, each one is just reflectivity.
The comparison carries the information
How the H and V returns differ — in strength, uniformity, and phase — reveals shape, variety, and rain.
Particles have shape
Raindrops flatten as they fall; hail tumbles; snow is irregular — two polarizations finally tell them apart.
Notes: Key intuition: it's the difference between H and V that's new, not the polarizations themselves. Keep it conceptual.

## Slide 29
The one idea: three new variables
ZDR — shape & size
How flattened the drops are
Big drops → high ZDR
Tumbling hail → near zero
ρhv — variety
How uniform the mix is
≈ 1 for pure rain
Low for hail, melt, non-weather
KDP — phase rain
A phase-based rain rate
Immune to attenuation
Fixes Block 4's shadow
Each maps to a widget: ZDR → drop shape · ρhv → particle variety · KDP → attenuation-proof rainfall.
Notes: The spine of the block. ZDR is shape, rho-hv is purity, KDP is the phase-based rain rate that pays off Block 4's attenuation.

## Slide 30
From “how much” to “what is it”
Tell things apart
Hail vs heavy rain, the melting layer, big drops — single-pol Z can't separate them; dual-pol can.
Flag non-weather
Birds, insects, and ground clutter show very low ρhv — easy to screen out.
Rescue rainfall
KDP measures rain through a phase that attenuation can't touch — the fix for Block 4's shadow.
Z says how much. Dual-pol says what it is.
Notes: Why it matters, in three payoffs: classification, quality control, and quantitative rainfall. The last one ties straight back to Block 4.

## Slide 31
What you'll do
Three widgets
ZDR & drop shape · ρhv & particle variety · KDP & attenuation-proof rainfall.
Real data
KTLX (Moore, 20 May 2013) — Z, ZDR, ρhv, and ΦDP of one storm, side by side.
TAKEAWAY
A single polarization tells you how much; two tell you what it is — ZDR reads shape, ρhv reads variety, KDP measures rain through attenuation.
Notes: Hand off to the notebook. Note this is the take-home bonus block — best worked at your own pace after the live session.

## Slide 32
Discussion
In the KTLX panels we used dual-pol to read one storm and found a 60 dBZ core that turned out to be heavy rain, not hail. What's a question someone might ask about a radar image that reflectivity alone can't settle, but dual-pol can?
Looking back across all five blocks, what's the one thing you'd want a colleague to keep in mind before trusting a single radar number?
Notes: Hand off to the notebook. Remind them to run the install and setup cells once, then work the widgets in order.